## Slide 1: Defense diploma thesis Daniel Fischer
Fakultät Maschinenwesen
Professur für Transportprozesse an Grenzflächen

## Slide 2: Content
Introduction
System
Governing equations
    Mesh dependency and validation
    Simulation results
    Conclusion & Outlook

## Slide 3: Introduction
Drive towards resource efficiency leads to the need of new materials
  Replacement of fossil based materials
  New regulations for environmentally harmful materials (PFAS, …)
Scale-up from lab to industrial/pilot scale needed
  Research in microfluidic systems
Previous research covers large time scales
  Interest in early time stages
  Interest in turning of gravity
Microfluidic element [1]
Microflow reactor [1]
Gravitational influence [2]

## Slide 4: Reaction-Diffusion-Advection fronts
RDA theory can be applied in various different fields
  Population dynamics
  Biological systems
  Geological systems
  Technological systems
Describe species distribution in space and time
ibz-freiberg.de
C
C
Brau, De Wit, J Chem Phys (2020)

## Slide 5: Taylor dispersion
Spreading property in space and time
  Spreading of a front within a pipe
  Spreading of gap averaged values

## Slide 6: system
Radial geometry
Domain filled with reactant A
Reactant B injected radially into B (A + B  C)
All species (A, B and C) have the same thermophysical properties
Gravitional forces are turned off
Axisymmetric assumption  2D Case sufficient to model
x
r
modelling plane
property | value
Molar mass [g/mol] | 100
Density [kg/m³] | 1000

## Slide 7: Governing equations
Mass conservation
  Continuity equation
  Momentum equations
        Radial momentum equation
        Axial momentum equation

## Slide 8: Governing equations
Species distribution equations
Reaction equation
  Reaction rate
      Reaction rate constant

## Slide 9: Mesh creation
case | n cells | cell size
h=0.2mm | 1.310.000 | 3e-6 [m]
h=0.4mm | 581.679 | 8e-6 [m]
h=0.6mm | 1.116.684 | 5e-6 [m]

## Slide 10: Boundary conditions
Inlet velocity magnitude
Lower limit: 8.33e-5 [m/s]
  0.047 [ml/min]
Upper limit: 4.21e-2 [m/s]
  0.793 [ml/min]
No slip
Pressure outlet
  20 [Pa]
  Isothermal
    300 [K]

## Slide 11: Mesh dependency and validation
Different mesh densities investigated
Validation against existing experimental data (Ý. Stergiou et al. 2023 (unpublished))

## Slide 12: Results

## Slide 13: Results

## Slide 14: Parametric study
Input variables
  Schmidt Number
        viscosity
        diffusion coefficient
  Peclet Number
        characteristic length (gap height)
        inlet velocity
        diffusion coefficient
Investigated parameters
  Fronts front & maximum positions
  Front widths
  Total product formed

## Slide 15: Front widths
Full Width at Half Maximum (FWHM)
Full Width at Half Maximum at Half Gap Height (FWHMHGH)
gap averaged concentration data
c [mol/l]
r [m]
FWHMHGH
Concentration data at half gap height

## Slide 16: Front positions h = 0.2mm
No change in principle behaviour based on Sc number
Pe influences front’s travelling speed

## Slide 17: Front widths h = 0.2mm
Clear Peak for FWHM at lower Schmidt number  Peak widens when Sc is increased
FWHMHGH grows toward final constant value in both cases

## Slide 18: Front widths h = 0.4mm
Peak is still visible for lower Sc number
For higher Sc FWHMHGH still in early growth phase

## Slide 19: Front widths h = 0.6mm
Wide spread peak for lower Sc (only clearly visible for highest Pe case)
FWHM growth delayed even more than for h = 0.4mm cases

## Slide 20: Total product formed h = 0.2mm
total product formed not influenced much by Sc or Pe
Sc influences the constant production rate towards the end

## Slide 21: Conclusion & Outlook
Outlook
  Further investigations possible with changing
        Inlet velocities
        Reaction rate/ Reaction mechanism
        Initial concentrations
        …
      Simulating the cases in 3D
      Providing simulation results for future experimental work
Conclusion
  Numerical model was developed and implemented in ANSYS FLUENT
  Validation done against experimental data
  Front properties do change dependent of the inlet conditions
  Significant influence of Sc on front properties
  Pe mostly influences the feature sharpness
1D
2D
3D

## Slide 22: Thank you for your attention

## Slide 23: Sources
[1] Corning AFR. Advanced fl ow reactors. https://www.corning.com/media/
worldwide/Innovation/documents/G1_WEB.pdf . Accessed: 2022-12-28.
[2] Yorgos Stergiou, Marcus JB Hauser, Alessandro Comolli, Anne Brau, Fabian and,
Gábor Schuszter, Paszkál Papp, Dezső Horváth, Clément Roux, Véronique
Pimienta, et al. Effects of gravity modulation on the dynamics of a radial a+
b→ c reaction front. Chemical Engineering Science, 257:117703, 2022.

## Slide 24: Governing equations
Energy equation

## Slide 25: Limitations
Limitations
  Simulating a 2D case
  Axisymmetric case
  Homogeneous velocity field at inlet
  Same physical properties
  Isothermal conditions

## Slide 26: parameters
Sc = 2430
Sc = 12000

## Slide 27: Front positions h = 0.4mm

## Slide 28: Front positions h = 0.6mm

## Slide 29: Total product formed h = 0.4mm

## Slide 30: Total product formed h = 0.6mm

## Slide 31: Velocity profile

## Slide 32: Width growth/shrinkage

## Slide 33: Experimental setup
Hele-Shaw-Cell with
  0.2mm gap height
  80mm radius
Reaction

## Slide 34: Residuals

## Slide 35: Gravitational influence

## Slide 36
Microfluidic element
Microflow reactor

## Slide 37: HPC Cluster